Washington State Gambling Commission

Shuffler Submission Checklist

Manufacturer:

Name and type of equipment:

Manufacturer representative name:

Manufacturer representative contact information:

WSGC only:

Submission #:

Date review begins:

Electronic Gambling Lab (EGL) representative:

Estimated hours to complete: 40 hours

Objective:

Our objective is to obtain detailed information about the equipment and to provide information about the minimum standards so that security, reliability, and integrity of the equipment are achieved. When manufacturers perform their own analysis of the equipment and provide this information to us, it often results in fewer questions to the manufacturer during testing and may reduce the overall review time. This checklist is a compilation of Washington laws and rules, best practices, and industry standards.

| Definitions: |  |
| --- | --- |
| Authentication | Process of determining if the source of the program is legitimate and valid. |
| Billing Purposes | Transmitting historical shuffler data that is used when billing is based on the number of successful shuffles. |
| Card Recognition | Ability to determine or recognize card information such as rank and suit. |
| Critical Memory | Memory locations storing data that is considered vital to the continued proper operation of the equipment. The contents of critical memory may include, but not be limited to, shuffler configuration data and game configuration data. |
| Electronic Card Shuffler | Electronic equipment that, at a minimum, has the capability to randomly rearrange a deck or decks of playing cards to completely eliminate any pattern(s) of the playing cards. |
| Error Condition | An internal or external event which results in an unexpected operational behavior or state. |
| External Tools | Trouble shooting programs that connect to the shuffler only via the Ethernet or USB port which are limited to laptops, tablets, USB products, or similar products approved by us. |

| Definitions: |  |
| --- | --- |
| Non Volatile Memory | Computer memory that can retain stored information even when powered off. |
| Random Number Generator (RNG) | Hardware, software, or a combination of equipment for generating number values that exhibit characteristics of randomness. |
| Secure Cellular Network | A secure cellular network includes the card shuffling device and a cellular modem that is used to transmit information via a secure cellular network. |
| Shuffle | Procedure of randomizing a deck or decks of playing cards to eliminate any prior pattern(s) introduced to the playing cards. |
| Verification | Process of checking that the content of the shuffler software is not corrupted. |
| Volatile Memory | Computer memory that requires power to maintain stored information; |

| The following sections must be completed by the Manufacturer. We require complete detailed answers. Yes/no answers will not be accepted. If this is a modification to an approved shuffler and you have already provided the information below, you may reference or attach the previous checklist to this submission. | WSGC Notes |
| --- | --- |
| General Submittal Questions |  |
| Submission Type: |  |
| Is this a new shuffler or a modification to an existing shuffler that has been previously tested and approved for use in Washington? |  |
| If this is a modification to a previously approved version, please provide a list of the changes below. |  |
| Please provide details on any modifications to the software that were due to known issues in the field or any other jurisdiction where the product has been/is deployed. |  |
| Shuffler Functionality |  |
| Review shuffler functionality: |  |
| Provide detail on how the shuffler meets the requirement of completely eliminating any patterns introduced to the playing cards. |  |
| Provide detail on how the shuffler refrains from leaving any markings or causing any damage to the playing cards that may help a player to identify any of the cards during normal shuffling operation. |  |
| The shuffler must not reveal the face value of cards at any time while in operation. Explain how your shuffler meets this requirement. |  |
| Does the shuffler produce reports and/or logs and if so where can they be found? Are they stored and if so, for how long? |  |
| Provide detail on how the shuffler indicates the current type of game being shuffled or dealt if it is capable of shuffling or dealing more than one type of game. |  |
| Does the shuffler have games built into the software or the ability to work with card games or bonuses of any type? If so, please provide a list of the games and bonus features below along with whether the game or bonus feature has been approved in Washington. |  |
| Does the shuffler include paytables for any games listed above? If so, please list the games below. |  |
| Can the shuffler be attached to a monitor or display that shows the results of games or shuffle information? If so, please provide details regarding the type of monitor/display, games that can be displayed and any additional software required for the information to be displayed. This includes other vendor’s equipment and/or software. |  |
| Provide a list or attach documentation of all functions and features available on this shuffler. “Available” functions and features are those capable of being activated by anyone after equipment has been delivered to the operator. |  |
| Software Requirements |  |
| Non Volatile Memory: |  |
| Provide detail on how the shuffler’s non volatile memory storage is maintained. Describe the process that enables errors to be identified and corrected. |  |
| Program Requirements: |  |
| Provide detail on how the shuffler software programs, including the RNG, are stored in media that prevent unauthorized access or alteration. |  |
| Provide detail on how PINS or passwords, if used, are protected and inaccessible. |  |
| Provide detail on whether the shuffler includes effective measures to ensure only authorized personnel can access restricted or sensitive settings within the software. |  |
| Independent Program Verification: |  |
| Any program verification used must have the ability to allow for independent authentication of the shuffler program (firmware and/or software). This authentication will provide a means for regulatory personnel to verify that the firmware and/or software operating on the shuffler is approved. |  |
| Communications: |  |
| Provide detail about the networking capabilities of the shuffler. |  |
| Provide detail about any external maintenance tool that will be connected to the shuffler for standard maintenance and how you ensure it will only be connected through a closed network. See WAC 230-16-151 – Standard maintenance and external tool requirements. |  |
| a. Provide detail on how the shuffler will be connected to a secure cellular network for billing purposes. Provide detail about how you will ensure that it complies with WAC 230-16-152 – Card shuffling devices connecting to a secure cellular network for billing purposes. The transmitted data must not include card specific information, live gaming data, or any other gambling information; and except for a confirmation notification from the network that the shuffler data was successfully received, there may only be one-way communication from the card shuffling device to the secure cellular network; and transmitted information may only be accessed by the licensee or licensed manufacturer; and a record must be kept of all information transmitted and made available to us upon request. |  |
| Restricted Access: |  |
| Provide detail about how unused internal and external ports can be disabled or sealed to prevent unauthorized access. |  |
| Provide detail on the peripheral equipment used with shufflers, including but not limited to, display monitors and input tools. Provide detail on how they work and how you ensure they work accurately. |  |
| Provide detail on how the peripheral equipment is resistant to tampering and unauthorized access. |  |
| Error Condition, Interruption and Resumption: |  |
| Provide detail about any indicators to signify the occurrence of an error condition. If the shuffler has a display screen, provide detail about the messages displayed describing the type of error. |  |
| Provide detail about the operation of the shuffler during an error condition (If an error condition causes the shuffler to malfunction, the shuffler must stop operating until the error condition is cleared). |  |
| Random Number Generator (RNG): |  |
| Explain how the RNG ensures the shuffling outcomes are: Statistically random; |  |
| Uniformly distributed, and |  |
| Unpredictable. |  |
| Provide detail about testing completed to ensure results of the RNG are accurately translated by the physical mechanisms of the shuffler. |  |
| Card Recognition: |  |
| Describe in detail any card recognition functionality and how you ensure accuracy. |  |
| Provide detail on any security measures that prevent a person or equipment from viewing information about cards which has not yet been revealed to all participants in a game. Card recognition information that has not yet been revealed must be stored in a volatile and secure memory space within the physical confines of the shuffler. |  |
| Hardware Requirements |  |
| Equipment Identification: |  |
| The shuffler must be identifiable with at least the following information: Name of the manufacturer; Unique serial number; and Model number; Provide the location of this information on the system. |  |
| Equipment Physical Construction: |  |
| Provide detail on the construction of the body of the shuffler. What material is used? Are all loose panels secured in a way to ensure that they have not been tampered with and do not conceal any hidden compartments? |  |
| Provide detail on how the shuffler is constructed in a manner that prevents unauthorized access to any critical area that includes software or hardware that impacts shuffle results. |  |
| WSGC only: Notes and additional testing parameters if needed. |  |